GRADING PERMIT

(The following is excerpted from the Ordinance # 01-18-2007A__________

(A)  Findings

The city has experienced development activity causing the displacement of large amounts of earth and the removal of vegetative cover.  Significant problems resulting from such development include flooding, soil erosion and sedimentation, unstable slopes, and impaired quality of life.  These problems are a concern because of their negative effects on the safety and general welfare of the community and environment.

(B)   Purpose

The purposes of this chapter are to:

- Prohibit the indiscriminate clearing of property.

- Prevent excessive grading, clearing, filling, cutting, or similar activities.

- Substantially reduce flooding, erosion and sediment damage within the city.

- To safeguard the safety and welfare of citizens.

- Establish reasonable standards and procedures for development, which prevent potential flooding, erosion and sediment damage.

- Prevent the pollution of streams, ponds and other watercourses by sediment.

- Minimize the danger of flood loss and property loss due to unstable slopes.

- Preserve natural vegetation, which enhances the quality of life of the community.

- To conceal hillside scars.

(C)  General requirements

- Persons engaged in land alteration activities regulated by this chapter shall take measures to protect neighboring public and private properties from damage by such activities.  The requirements of this chapter, however, are not intended to prevent the reasonable use of properties.

- The responsible party shall be liable for all fines levied or remedial action required under this chapter.  Each violation shall be considered a separate offense.

- Any person, who engages in land alteration activities regulated by this chapter without obtaining a grading permit, shall be required to restore the land, to the maximum extent practicable to its original condition.

- The permit applicant shall have on the project site at all times an agent who is a competent superintendent capable of reading and thoroughly understanding the plans, specifications and requirements for the type of work being performed.  The superintendent shall have full authority to issue orders or direction to employees working on site, without delay and to promptly supply such materials, labor, equipment, tools, and incidentals as may be required to complete the work in a proper manner.  If no superintendent is on site, the city official may issue the notice of violation and stop work order to the person conducting the violation.

(D)	Grading Permit Required

- Any person proposing to engage in clearing, filling, cutting, quarrying, construction or similar activities on any piece of disturbed land of 1 acre or larger shall apply to the City for a grading permit as specified in this chapter.  A large scale development plan shall be approved by the City before constructing or expanding a vehicular use area or when expanding or rehabilitating a building and landscaping is required.  No land shall be altered or cleared to the extent regulated in this chapter unless approved by a permit.

- No land alteration shall be permitted until all necessary city approval of all plans and permits, except building permit, have been issued and construction is imminent.  In those cases where filling or cutting in areas with no trees is to be done, the area is to be graded suitable for mowing and shall be re-vegetated.

- A grading permit is required for land alteration activities specified in this section.  However, all construction work shall include appropriate drainage and erosion control measures to protect neighboring properties.  All land alteration in properties within the designated 100 year floodplain or on a 20% or greater slope and any excavation from which fill will be exported or imported requires a grading permit without exception.

- Prior to issuance of a grading permit, a grading and drainage plan shall be submitted and approved by the City.  A drainage report shall be submitted to the city at the time new subdivisions and large scale developments are submitted for project approval.  The drainage report shall comply with all current drainage ordinances and must be certified by a registered professional engineer licensed in the State of Arkansas.

- Utility organizations may obtain a one-time approval from the City for all routine tree trimming and installation, maintenance, replacement and repair of fence and sign posts, telephone poles and other kinds of posts or poles and overhead or underground electric, water, sewer, natural gas, telephone or cable facilities.  The approval will include a utility organization and its contractors, agents or assigns and will be permanent in nature as long as the original approved procedures are followed.  However, large-scale utility projects involving clearing of areas over twenty-five (25) feet in width shall not be authorized by one-time approval of all projects.  In such cases, a separate grading permit must be obtained for each project.

- One-time approval may be obtained by public or private entities for the stockpiling of construction spoil material at particular locations for a limited time period, not to exceed six (6) months.  Grading and replanting of grassed areas is required upon removal of stockpile.

(E)	Exemptions

A grading permit shall not be required for:

- Emergency work or repairs to protect health, safety and welfare of the public.

- Cemetery graves.

- Construction of or addition to a single family residence.  This shall include excavations for basements, footings, swimming pools, hot tubs septic systems, retaining walls, and like structures.

- Refuse disposal sites controlled by other regulations.

(F)  Contents of grading plans

The grading and drainage plan shall identify the following:

- Acreage of the proposed project.

- Designate all land areas to be disturbed and label acreage of disturbed areas.

- Stages of grading showing the limits of sections to be graded.

- The height and slope of cuts and fills.

- Cross sections shall be required every one hundred fifty (150) feet on property where the depth of excavation or fills exceeds five (5) feet, showing original and final grades.  A grading plan showing existing and proposed contours with a maximum 2-foot contour interval for slopes less than 10% and a maximum 5-foot contour interval for slopes greater than 10% can be shown as an alternate to cross-sections every 50 feet.

- Provisions for collecting and discharging surface water.

- Erosion and sediment control measures, including structural and vegetative measures.  Specification of measures to control runoff, erosion and sedimentation during the process of construction, noting those areas where control of runoff will be required during construction and indicating what will be used, such as sediment basins, silt dams, rock check dams, lateral hillside ditches, catch basins, etc.

- Seal, Certificate of Authority and signature of a registered engineer qualified under state regulations to certify that the grading and drainage plan complies with this chapter.

- A vicinity drawing showing location of property lines, location and names of all existing or platted streets or other public ways within or immediately adjacent to the tract on City of Elkins topographic mapping or approved equal.

- Location of all known existing sewers, water mains, culverts and underground utilities within the tract and immediately adjacent thereto; location of existing permanent buildings on or immediately adjacent to the site if right of entry can be obtained to locate same.

- Identification of rights-of-way or easements affecting the property.

- A plan of the site at a minimum scale of one (1) inch equals one hundred (100) feet or less, i.e. 1” = 50’ or 1” = 30’, etc.

- The grading plan shall include areas of tree protection, erosion and sediment control provisions meeting standards established by the City and ADEQ.

Such other information required by the City, including but not limited to:

- The approximate location and width of existing and proposed streets.

- The locations and dimensions of all proposed or existing lots.

- The locations and dimensions of all parcels of land proposed to be set aside for parks, playgrounds, natural condition perimeters, public use, or for the use of property owners in proposed development.

- Existing and proposed topography at a maximum of two-foot contour intervals unless approved otherwise by the City.

- Identification of unusual material or soils in land areas to be disturbed.  If any surface indications of unusual materials or soils that would cause street or lot instability, such as non-vertical tree growth, old slides, seepage, or depressions in the soil are visible before grading, they should be noted and accompanied by the engineer’s recommendation for correcting such problem areas.

- Identification of suitable material to be used for fills shall be accomplished before actual filling begins.  If there are any surface indications that local material is not suitable for fills, those areas to be filled with outside material should be identified and the type and source of the fill noted.

- Measures to protect neighboring built-up areas and city property during process of construction, noting work to be performed, such as cleaning existing ditches, storm culverts and catch basins or raising existing curbs in neighboring areas.

- Provisions to stabilize soils and slopes after completion of streets, sewers and other improvements, noting on the grading plan when and where ground cover will be planted, also noting any other means to be used such as placement of stone embankments and riprap or construction of retaining walls.

- All fill areas shall be compacted to 95% standard proctor density unless approved otherwise.

(G)  Issuance procedure

The following procedure shall be implemented for the issuance of a grading permit.

- The City or its authorized representative shall approve, disapprove or recommend modification of the grading plan in writing within ten (10) working days after the date of submittal.

- Upon approval of the final plan, the City shall issue a grading permit.  A superintendent capable of understanding the plans and with the authority to issue orders to employees performing the land alteration shall properly supervise the land alteration work.

Groups of trees and individual trees that are not to be removed and required undisturbed buffer areas shall be protected during construction by protective fencing and shall not be used for material storage or for any other purpose.  The fencing shall be placed and maintained by the owner until all exterior construction except landscaping has been completed.  Individual trees to be preserved outside the protected area shall be fenced at the critical root zone and shall be flagged with bright orange vinyl tape wrapped around the main trunk at a height of four (4) feet or more such that the tape is clearly visible to workers on foot or operating equipment.

The Planning Department Leader may allow minor modifications of the plan to alleviate particular problems during the process of construction.  In reviewing request for modifications, the Planning Department Leader may require from the applicant’s engineer appropriate reports and data sufficient to make a decision on the request.

Major changes to plans previously approved shall only be permitted by the planning commission.  Examples of major changes are those that substantially increase the height of cuts, the area of clearing or grading, or impact on neighboring properties.  More than twenty percent (20%) increase in height, area or impact will normally be considered a major change.  Examples of increased impact include reductions in buffer area, increased runoff onto adjacent properties and increased site area that is visible from adjacent properties or public streets.

(H)  Grading plan requirements

- Preparation of grading and drainage plans shall be designed on the basis of the following considerations:

  - A maximum of thirty (30) vertical feet of fill or excavation (three, ten [10] feet vertical terraces or two, fifteen [15] feet vertical terraces) is permitted.  However, additional development areas may be constructed a minimum of one-hundred fifty (150) feet in width and at a slope of no more than eight percent (8%).  The maximum of thirty (30) feet of fill or excavation may again be utilized.

  - The depth of fill or excavation shall be measured from the finish grade elevation to the original ground line elevation.

  - No more than two hundred (200) feet of terrace can be in a straight line and a minimum of a ten (10) foot curved section, jog, or offset is required for each additional 200 feet of terrace.

  - For excavations or fills constructed with slopes flatter than 3:1 (three horizontal to one vertical), terraces are not required nor is there a limit on the height of cut of fill.  Planting requirements on these 3:1 slopes shall be the same as required for terraces and shall be spaced uniformly over the slope.

  - Cuts or fills shall be limited to ten (10) feet in height or to fifteen (15) feet if architectural stone is included to protect the vertical face.  A series of smaller cuts or fills with terraces, preserving portions of natural vegetation and providing areas for planting, shall be used in situations where more than ten (10) feet of cut or fill is needed.

  - Terracing width shall be at a ratio of at least one (1) foot of horizontal terrace for every one (1) foot of vertical height, up to a maximum of ten (10) feet.  Terraces shall be landscaped with dense evergreen plantings sufficient to screen the cut or fill slope.

  - If the slope of the cut or fill is faced with an architectural stone wall, the terrace plantings shall be a minimum of two (2) rows of trees four (4) feet between the rows, staggered not more than twenty (20) feet on centers.

- Development shall be planned to fit topography, soils, geology, hydrology, and other existing site conditions.

- To the extent practical, lot boundaries shall be made to coincide with natural and pre-existing man-made drainage ways within subdivisions.

- Provisions shall be made for safety against unstable slopes or slopes subject to erosion and deterioration.

- Grading shall complement natural landforms.

- Easements for drainage channel maintenance shall be in accordance with the current drainage ordinance.

- All developments or any lot containing or adjacent to a drainage channel or drainage structure must provide the minimum finish floor elevation for any proposed structure based on the 100 year flood elevation in the drainage structure.  For subdivisions, this minimum elevation shall be shown on the Final Plat.  For Large Scale Development Plans, this minimum elevation must be shown on the approved plans.

- After grading, all paving, seeding, sodding, or mulching shall be performed in accordance with a reasonable schedule approved by the Planning Department Leader.

- Open areas not planned for immediate use shall be seeded or sodded.  Soil which is exposed for more than twenty-one (21) days with no construction activity shall be seeded, mulched or re-vegetated in accordance with this code.  All restoration efforts must be to the satisfaction of the City.

- Areas not well suited to development, as evidenced by existing incompetent soils, geology, hydrology investigations and reports, should be allocated to open space and recreational uses.

- The potential for soil loss shall be minimized by retaining natural vegetation wherever possible.

- Appropriate BMPs and other erosion and sediment control practices shall be used to accommodate stormwater runoff and control soil loss occasioned by changed soil and surface conditions during and after development, including the use of vegetation and limitations on soil exposure.  If staff determines upon visual inspection that excessive silt from the construction has migrated offsite, additional measures to reduce erosion may be required.

- Permanent improvements such as streets, storm sewers, curb and gutters and other features for control of storm runoff shall be scheduled as soon as economically and physically feasible before removing vegetation cover from the area, so that large areas are not left bare and exposed for long periods of time beyond the capacity of temporary control measures.

- Private roads, parking lots, and access ways (excluding residential driveways), within developments shall utilize curb, gutter, and storm drain systems to provide adequate drainage.  The use of swales and siding open side ditches are acceptable only upon written approval of the Planning Department Leader.  All utilities must be a minimum of 24” below the flow line of an open ditch unless approved in writing by the Planning Department Leader and the respective utility company.  Clearances may be reduced for paved ditches.

- Persons engaged in land alteration activities regulated by this chapter shall take measures to protect public and private properties from damage by such activities.

- A temporary or permanent sediment basin, debris basin, silt basin or silt trap shall be installed and maintained to substantially reduce sediment from water runoff.  The volume of the sediment basin shall be three-thousand (3000) cubic feet per acre for property with average slope greater than five (5) percent, or fifteen-hundred (1500) cubic feet per acre for property with an average slope less than five (5) percent.  A properly sized sediment basin is required for each separate drainage area within the property being developed.

- Construction access shall be limited to locations as approved by the City. Construction access points shall be graveled for a minimum length of twenty percent (20%) of the lot depth or fifty (50) feet, whichever is greater, up to a maximum of one hundred (100) feet and of adequate thickness to minimize tracking onto the city street.  Two (2) to three (3) inch crushed stone shall be used for the construction entrance.

- Appropriate provisions shall be made to prevent excessive particulate matter from becoming airborne.

- A perimeter buffer strip shall be temporarily maintained around disturbed areas for erosion control purposes and shall be kept undisturbed except for reasonable access for maintenance.  The width of the strip shall be six percent (6%) of the lot width and depth.  The minimum width shall be twenty-five (25) feet and the maximum shall be forty (40) feet.  In no event shall these temporary strips be less than the width of the permanent buffers required for the development.

- A minimum strip twenty-five (25) feet wide, undisturbed except for reasonable access, shall be provided along each side of streams having a peak ten-year storm flow rate of greater than one hundred fifty (150) cubic feet per second. The 25-foot strip shall be measured from the top of the bank.  An exception to this requirement is allowed where the only work being done on the site is public street construction.

- Care shall be exercised to minimize the risk of damage from or to pedestrian and vehicular traffic in the vicinity of a cut or fill by placement of handrails, guardrails, fencing or landscaping.

(I)  Unified plan and permit

One plan may be submitted incorporating all provisions for compliance with the applicable city zoning, drainage, stormwater detention, grading, clearing, filling, cutting, quarrying, and construction requirements.

(J)  Miscellaneous

- Grading plans shall conform to the Phase II Stormwater Regulations as established by United States Environmental Protection Agency’s regulations, Region VI published in the July 6, 1998 Federal Register or its latest revisions.

- A copy of the ADEQ NOI permit shall be required for all sites of one (1) acre or more.

(K) Transition Period

Any construction or development project which has received a development or building permit under prior provisions of the Elkins Code shall come into full compliance with the requirements of this ordinance within thirty (30) days of its effective date.

(L)  Fees

A fee for each grading permit shall be paid to the city as follows:

Total Project Area				                                     Fee

1 acre or less …………………………..	 $100.00

(Or actual costs if an engineer or other professional is consulted by the

Planning Department Leader in approving/considering the grading permit)

Greater than1 acre but less than 5 acres	$200.00

(Or actual costs if an engineer or other professional is consulted by the

Planning Department Leader in approving/considering the grading permit)

Greater than 5 acres	$300.00

(Or actual costs if an engineer or other professional is consulted by the

Planning Department Leader in approving/considering the grading permit